## Slide 1
Parallelized Discrete Event Simulator for VHDL
FINAL REVIEW · PHASE 2
Event-driven logic simulation · OpenMP parallelism · Delta-cycle semantics
2025MCS2105 · 2025MCS2094
IIT Delhi · M.Tech Cornerstone Project
01 / 18

## Slide 2
Phase 1 Recap
FOUNDATION FROM THE MIDSEM REVIEW
▸ Event-driven engine with delta cycles — guarantees VHDL causality at T=T₀
▸ Flex + Bison VHDL frontend → AST → code-generated netlist (.net) and stimulus (.stim)
▸ Double-buffered Signal class: getValue() reads current, scheduleUpdate() writes next
▸ Priority queue keyed on (time, delta) for deterministic event ordering
▸ VCD writer produces IEEE-1364 compliant waveforms for GTKWave inspection
IIT Delhi · M.Tech Cornerstone Project
02 / 18

## Slide 3
System Architecture
END-TO-END DATA FLOW
VHDL (.vhd)
Flex Lexer
Bison Parser
AST
CodeGen
Netlist (.net) Stimulus (.stim)
.net / .stim
Build DAG + Layer (Kahn)
Parallel Delta-Cycle Loop
Commit + Schedule
VCD Output
Frontend (row 1) emits a flat netlist; engine (row 2) topologically layers it and runs the delta-cycle loop in parallel.
IIT Delhi · M.Tech Cornerstone Project
03 / 18

## Slide 4
What's New in Phase 2
SCOPE OF DELIVERABLES
▸ Kahn-layered parallel execution — O(V+E) topological sort over the netlist DAG
▸ Dedicated -seq runtime flag: bypasses all OpenMP pragmas for a clean baseline
▸ Six optimization trials with measured deltas — two kept, four rejected
▸ Parallel commit phase with PARALLEL_THRESHOLD gate and dynamic schedule(16)
▸ Tkinter benchmarking dashboard (stdlib only, zero pip dependencies)
▸ Sequential-vs-parallel bit-identity test harness (VCD byte-diff per circuit)
IIT Delhi · M.Tech Cornerstone Project
04 / 18

## Slide 5
Kahn-Layered DAG
DEPENDENCY ANALYSIS FOR PARALLEL DISPATCH
▸ Each process P lives in a layer L(P) = max(L(q)) + 1 ∀ q ∈ inputs(P)
▸ Topological layering via modified Kahn — complexity O(V + E)
▸ Intra-layer processes share no signal dependencies ⇒ race-free parallelism
▸ Engine issues one #pragma omp parallel for per layer sequentially
▸ Layer width = max parallelism budget at that depth
Inputs
P0
P1
P2
P3
P4
P5
P6
Outputs
Layer 0
Layer 1
IIT Delhi · M.Tech Cornerstone Project
05 / 18

## Slide 6
Layer Assignment
IMPLEMENTATION SKETCH OF KAHN'S ALGORITHM
▸ indeg[v] = number of unique input signals of process v
▸ Initial frontier: processes with no predecessors (fed only by inputs)
▸ BFS walk updates layer[v] = max(layer[v], layer[u]+1) for each fanout
▸ Cycles detected by left-over non-zero indeg; pushed to a fallback layer
▸ Final layers[] grouped into a vector<vector<Process*>> for dispatch
// Topological layering
for (auto& v : processes) indeg[v] = v->inputs.size();
queue<Process*> Q;
for (auto& v : processes)
if (indeg[v] == 0) { layer[v] = 0; Q.push(v); }
while (!Q.empty()) {
auto v = Q.front(); Q.pop();
layers[layer[v]].push_back(v);
for (auto* u : fanout(v)) {
layer[u] = max(layer[u], layer[v]+1);
if (--indeg[u] == 0) Q.push(u);
}
}
// dispatch
for (auto& L : layers)
#pragma omp parallel for
for (size_t i = 0; i < L.size(); i++)
L[i]->evaluate();
IIT Delhi · M.Tech Cornerstone Project
06 / 18

## Slide 7
Parallel Simulation Loop
PER TIME-STEP STATE MACHINE
SEQUENTIAL
1. Drain events
Pop all events with (t=current, δ) from the priority queue.
PARALLEL
2. Evaluate
For each layer L: #pragma omp parallel for over processes in L.
PARALLEL
3. Commit
Swap next→current on every Signal; collect changed_flags[].
SEQUENTIAL
4. Reschedule
For each changed signal, enqueue its sensitive processes at δ+1.
↻ Repeat until no signal changes at current time; then advance simulation clock.
IIT Delhi · M.Tech Cornerstone Project
07 / 18

## Slide 8
Double-Buffered Signal
LOCK-FREE WRITE/READ SEPARATION
▸ Every Signal stores current_value (read) and next_value (pending)
▸ Evaluation: processes read current, call scheduleUpdate(v) → writes next
▸ Reads in one delta never observe partial writes of the same delta
▸ commit() atomically copies next → current and returns true if changed
▸ No mutex on the hot path — only a parallel scan over signals in the commit phase
EVALUATE (delta k)
COMMIT (end of delta k)
Process A
Process B
cur
nxt
Signal
read
write
commit():
next → current (atomic)
cur'
—
Signal (delta k+1)
When |signals| ≥ PARALLEL_THRESHOLD (512), commit scan runs under #pragma omp parallel for schedule(dynamic, 16).
IIT Delhi · M.Tech Cornerstone Project
08 / 18

## Slide 9
Sequential Baseline ( -seq )
WHY AN EXPLICIT MODE MATTERS
▸ OpenMP at OMP_NUM_THREADS=1 still pays for parallel-region setup and barriers
▸ Measured overhead: 3-8% on small circuits; swamps real gains below ~500 gates
▸ -seq takes the single-branch code path in Simulator::run() — no parallel regions hit
▸ Separates 'did we speed up?' from 'did we amortise OpenMP fork/join?'
▸ Reported speedup: S(N) = T_seq / T_N, using the simulator-internal Elapsed timer
▸ T_seq is also the reference for correctness: every parallel VCD must byte-match it
IIT Delhi · M.Tech Cornerstone Project
09 / 18

## Slide 10
Optimization Trials
SIX EXPERIMENTS · TWO KEPT
TRIAL
KEPT
RATIONALE
PARALLEL_THRESHOLD gate (512)
Yes
Skip #pragma omp for small signal sets; ~5% win on tiny designs
Parallel commit scan
Yes
schedule(dynamic, 16); commit was 30%+ of runtime at high N
OpenMP task scheduling
No
Per-process tasks underperformed static parallel-for on balanced DAGs
Per-layer thread-count tuning
No
<3% gain vs autoscale; added configuration surface
Lock-free event queue
No
Priority-queue invariants hard to preserve under concurrent push/pop
Signal batching by owner
No
Cache locality gain < memcpy cost for batched next-value buffers
IIT Delhi · M.Tech Cornerstone Project
10 / 18

## Slide 11
Benchmark Setup
REPRODUCIBILITY DETAILS
HARDWARE / TOOLCHAIN
CPU
AMD Ryzen 7 7735HS
Cores / Threads
8C / 16T @ 3.2 GHz base
Compiler
g++ 13, -O2 -fopenmp
OS
Linux 6.x native
Circuits
15 (.vhd in test_vhdl/)
MEASUREMENT PROTOCOL
OMP_WAIT_POLICY
active
OMP_PROC_BIND
true
Thread sweep
seq, 1, 2, 3, 4, 5, 6, 7, 8
Repeats
3 · fastest kept
Timer source
Simulator::run() Elapsed (ms)
IIT Delhi · M.Tech Cornerstone Project
11 / 18

## Slide 12
Speedup — pyramid_100k
DEEP PYRAMID NETLIST · BASELINE T_SEQ = 1371 MS
0.5×
1.0×
1.5×
2.0×
2.5×
0.98×
1T
1.43×
2T
1.75×
3T
1.97×
4T
2.07×
5T
2.22×
6T
2.30×
7T
2.38×
8T
Scaling is sub-linear: Amdahl bound ≈ critical-path depth / total processes.
IIT Delhi · M.Tech Cornerstone Project
12 / 18

## Slide 13
Efficiency Across Circuits
SPEEDUP / THREADS
CIRCUIT
SEQ (MS)
2T
4T
6T
8T
pyramid_100k
1371.0
0.71
0.49
0.37
0.30
pyramid_and_tree
461.9
0.74
0.51
0.38
0.30
large_wide_and_tree
6.46
0.56
0.29
0.19
0.12
large_alu_8bit
2.80
0.47
0.27
0.18
0.12
large_wide_mixed_gates
4.88
0.53
0.27
0.10
0.14
full_adder
0.15
0.45
0.24
0.17
0.08
Efficiency = Speedup / N. Large pyramids sustain >0.3 at 8T; small circuits collapse because parallel-region cost dominates.
IIT Delhi · M.Tech Cornerstone Project
13 / 18

## Slide 14
Benchmarking Dashboard
TKINTER GUI — ZERO PIP DEPENDENCIES
▸ Pure stdlib: tkinter, subprocess, threading, queue — runs on any Python 3.9+
▸ File upload or bundled-example picker; run single config or thread sweep
▸ Sweep auto-runs -seq baseline first, then threads 1..N (no -seq) for honest data
▸ Live charts: wall-time, speedup, efficiency — updated from worker-thread queue
▸ One-click GTKWave launch on the fastest VCD of a sweep
▸ Auto-detects simulator binary (Linux or MSYS/MinGW) relative to the script
[ dashboard.png ]
(drop a screenshot onto this box)
IIT Delhi · M.Tech Cornerstone Project
14 / 18

## Slide 15
Testing Methodology
CORRECTNESS-FIRST VALIDATION
▸ Bit-identity: VCD(parallel, N threads) ≡ VCD(-seq) — byte-for-byte
▸ 36 assertion tests covering 12 gate primitives + sequential elements (DFF, Latch)
▸ VHDL frontend: lexer / parser / codegen round-trip across 15 reference circuits
▸ Regression harness: make test runs on every commit, fails on any VCD diff
▸ Tests automatically sweep threads ∈ {1, 2, 4, 8} to catch race regressions early
IIT Delhi · M.Tech Cornerstone Project
15 / 18

## Slide 16
Limitations
KNOWN GAPS AND CAVEATS
▸ ClockProcess: delta-0 ordering not fully deterministic under high thread counts
▸ Cyclic netlists collapse into a fallback single-layer (lose parallelism for that region)
▸ Small designs (<500 gates): parallel-region cost > work; -seq faster in practice
▸ No incremental recompile of VHDL — full flex/bison rebuild on every change
▸ VCD writer is single-threaded (Amdahl floor on I/O-heavy runs)
IIT Delhi · M.Tech Cornerstone Project
16 / 18

## Slide 17
Contributions
TEAM BREAKDOWN
2025MCS2105
▸ Core simulator engine (C++17) and OpenMP integration
▸ Double-buffered Signal class; commit phase parallelisation
▸ Benchmark harness, optimization trials and analysis
▸ -seq baseline mode and speedup instrumentation
2025MCS2094
▸ VHDL frontend — Flex lexer, Bison grammar, AST walker
▸ Netlist code generator (.net / .stim emission)
▸ Kahn-layering and DAG construction in the engine
▸ Tkinter dashboard and regression-test harness
IIT Delhi · M.Tech Cornerstone Project
17 / 18

## Slide 18
Conclusion & Future Work
WRAP-UP
01
Kahn layering + double-buffered signals give deterministic parallelism
02
Explicit -seq baseline exposes real scaling, not OpenMP overhead
03
Benchmark-driven search rejected four of six candidate optimizations
FUTURE WORK
▸ Feedback-cycle breaking (SCCs → heuristic serialisation)
▸ Adaptive OMP thread count per-layer (layer width heuristic)
▸ GPU offload for wide combinational layers (CUDA kernels)
▸ Richer VHDL grammar: generate, generic maps, multi-wait
Questions?
IIT Delhi · M.Tech Cornerstone Project
18 / 18